List of Symbols used in:

1D SEDIMENT TRANSPORT MORPHODYNAMICS

with applications to

RIVERS AND TURBIDITY CURRENTS

NOTE  Occasionally one symbol is used for two different parameters with different definitions.  When this is the case the second definition is given in red.

Symbol		Definition and Dimensions (L = length, T = time, M = mass,

1 = dimensionless)

au			upwinding coefficient in spatial finite difference scheme [1]

B			channel width [L]; also dimensionless coefficient in

generalized logarithmic law of the wall [1]

Bb			width of bed region of channel [L]

Bbf			channel width at bankfull flow [L]

Bf			floodplain width (excluding channel) [L]

Bs			width of sidewall region of channel (one of the sidewalls) [L]

= Bbf/Ds50; dimensionless bankfull width [1]

b			reference distance above the bed where sediment

entrainment is specified; b/H << 1 [L]

C			= depth-flux averaged (river) or layer-flux averaged (turbidity

current) volume concentration of suspended sediment

[1]

Cf			= (b/((U2), bed friction coefficient [1]

Cff			friction coefficient due to form drag [1]

Cfs			friction coefficient due to skin friction [1]

Ct			= qt/(qt + qw), flux-based volume concentration of sediment

(bedload + suspended load) [1]

Cwi			volume concentration of wash load in the ith grain size range

[1]

Cz			, dimensionless Chezy resistance coefficient

[1]

Czbf			= , bankfull estimate of Cz [1]

Czs			= , Chezy resistance coefficient due to skin friction [1]

c			volume concentration of suspended sediment [1]

volume concentration of suspended sediment averaged over

turbulence [1]

fluctuating component of volume concentration of suspended

sediment [1]

upward normal Reynolds flux of suspended sediment due to

turbulence [L/T]

volume concentration of suspended sediment in the ith grain

size range averaged over turbulence [1]

near-bed value of  at z = b [1]

near-bed value of  at z = b [1]

cD			dimensionless fluid drag coefficient for a sediment particle

[1]

dimensionless wave speed used in Chapter 20 [1]

D			grain size (usually in mm or (m) [L]

Db,i			ith bounding size specifying percents or fractions finer of

grain size distribution [L]

Dg			geometric mean grain size [L]

Di			characteristic size of the ith sediment size range [L]

Dlg			geometric mean size of load [L]

Dsg			geometric mean size of surface layer sediment [L]

D50			median grain size [L]

D90			sediment size such that 90 % of the material in the sample is

finer [L]

Dl50			median size of load [L]

Dl90			sediment size such that 90 % of the material in the load is

finer [L]

Ds50			median size of surface layer sediment [L]

Ds90			sediment size such that 90 % of the material in the surface

layer is finer [L]

Ds			volume rate of bed deposition from suspension per unit bed

area per unit time [L/T]

Dx	sediment size such that x % of the material in the

sample is finer [L]

E	= Es/vs, dimensionless rate of entrainment of bed sediment

into suspension [1]

Ebl	volume rate of entrainment of bed particles into bedload

transport per unit bed area per unit time [L/T]

Ei	dimensionless rate of entrainment of bed sediment from the

ith grain size range into suspension [1]

Es	volume rate of entrainment of bed sediment into suspension

per unit bed area per unit time [L/T]

Esi	volume rate of entrainment of bed sediment from the ith grain size range into suspension per unit bed area per unit time [L/T]

Fc	Coulomb resistive force acting on a particle [ML/T2]

FD	fluid drag force acting on a particle [ML/T2]

Fg	gravitational force acting on a particle [ML/T2]

Fgn	component of force Fg acting normal to the bed [ML/T2]

Fgt	component of force Fg acting tangential to the bed [ML/T2]

Fi	fraction of sediment in the ith grain size range of the surface

layer [1]

Fp	pressure force [ML/T2]

Fr	, Froude number [1]

Frbf	, bankfull Froude number [1]

Fro	; Froude number of unperturbed flow [1]

Fs	mass fraction of the surface sediment that is sand [1]

fbb	fraction of eroded sidewall material that is coarse enough to

move as bed material load [1]

ff,i			mass fraction in sample that is finer than size Db,I [1]

fi			fraction of sediment in the ith grain size range; fraction of

sediment in ith grain size range of substrate [1]

fIi			fraction of material in the ith grain size range that is

exchanged across the surface-substrate interface as

the bed aggrades or degrades [1]

fraction of sediment in the ith grain size range (function of z)

[1]

G(()			function in Parker (1990a,b) and Wilcock and Crowe (2003)

bedload relation for gravel 	mixtures; the function is

different in each case [1]

Gt			total mean annual bed material load in million tons per year

[M/T]

g			acceleration of gravity [L/T2]

gb			mass bedload transport rate per unit width [M/L/T]

H			cross-sectionally averaged flow depth (river) or flow

thickness (turbidity current) [L]

Hbf			bankfull cross sectionally-averaged flow depth [L]

Hc			critical depth at a Froude number of unity [L]

Hf			depth associated with form drag [L]

Hn			normal depth [L]

Hs			depth associated with skin friction [L]

Ho			constant channel depth of the unperturbed base flow, used

- to study bedforms and b) to develop the quasi-

- steady approximation [L]

= Hbf/Ds50, dimensionless bankfull depth [1]; also = H/D50 in

Ackers-White (1973) and Brownlie (1981) relations for

total bed material load [1]

= H/Ho, dimensionless depth for study of bedforms [1]

= H/Ho, dimensionless depth [1]

= dimensionless deviatoric depth [1]

= ; dimensionless depth perturbation for study of

bedforms [1]

amplitude of dimensionless depth perturbation [1]

If			intermittency factor; the river is in flood (and

morphologically active) for time fraction If [1]

Is			volume rate of input of sediment to channel from sidewalls

per unit streamwise length of channel per unit time

[L2/T]

kc			composite roughness height associated with both skin

friction and form drag [L]

k			= 2(Ho/(; dimensionless wavenumber of bed wave with

wavelength ( [1]

ks			grain roughness height associated with skin friction [L]

L			reach length [L]

La			thickness of active (surface, exchange) layer [L]

Lb			backwater length [L]

Lsr			relaxation, or adaptation distance associated with the

development of an equilibrium profile of suspended

sediment concentration, defined in Chapter 21 [L]

na			dimensionless parameter such that La = naDs90 [1]

Lsbl			mean step length of a bedload particle [L]

nk			parameter such that ks = nk Ds90 [1]

nt			exponent in generic relation for total bed material load [1]

p			pressure [M/L/T2]

pai			fraction of bedload in the ith grain size range, averaged over

the flow duration curve [1]

pi			fraction of bedload in the ith grain size range [1]

pQk			fraction of time the flow is in the kth discharge range of the

flow duration curve [1]

Q			flow discharge [L3/T]

Qbf			bankfull flow discharge [L3/T]

Qk			characteristic flow discharge for the kth range of the flow

duration curve [L3/T]

Qm			momentum discharge [ML/T2]

Qtanav			annual average total volume bed material load [L3/T]

Qt			total volume bed material load [L3/T]

Qtbf			total volume bed material load at bankfull flow [L3/T]

Qt,k			total volume bed material load at the kth characteristic flow

of the flow duration curve [L3/T]

= ; dimensionless bankfull discharge [1]

qb			volume bedload transport rate per unit width [L2/T]

qbi			volume bedload transport rate per unit width in the ith grain

size range [L2/T]

qbT			= (qbi, total volume bedload transport rate summed over all

grain size ranges [L2/T]

qs			volume suspended load transport rate per unit width [L2/T]

qsi			volume suspended load transport rate per unit width in the

ith grain size range [L2/T]

qt			= qb + qs, volume total bed material transport rate per unit

width [L2/T]

qtf			volume feed rate per unit width of total bed material load

[L2/T]

qts			volume rate of supply per unit width of total bed material load

used in study of bedrock rivers [L2/T]

qto			unperturbed value of qt at base equilibrium [L2/T]

qw			water discharge per unit width [L2/T]

= , Einstein number for bedload transport [1]

= , Einstein bedload number for ith grain

size [1]

= , Einstein number for total bed material

load [1]

= , [1]

= qt/qto, dimensionless total bed material transport [1]

R			= ((/(s – 1), sediment submerged specific gravity [1]

Rh			hydraulic radius [L]

Rep			=  [1]

Rep50			=  [1]

Repi			=  [1]

Revp			=  [1]

Rf			= , fall number [1]

Rif			flux Richardson number [1]

Ri 			gradient Richardson number [1]

S			= - ((/(x, down-channel bed slope [1]

Sb			slope of bedrock basement [1]

Sf			down-channel friction slope [1]

SI			initial down-channel bed slope [1]

Sinit			initial down-channel bed slope [1]

So			unperturbed value of bed slope S of base equilibrium [1]

Ss			transverse slope of sidewall region of channel [1]

sba			streamwise position of the bedrock-alluvial transition [L]

t			time [T]

tf			= Ift, flood time [T]

= Uot/Ho, dimensionless time used in developing the quasi-

steady approximation [1]

= , dimensionless morphodynamic time used in

developing the quasi-steady approximation [1]

transformed time used in moving-boundary formulations [T]

, dimensionless time used in Chapter 20

[1]

U			depth- or cross sectionally-averaged flow velocity (river) or

layer-averaged velocity (turbidity current) [L/T]

Ubf			bankfull depth- or cross sectionally-averaged flow velocity

[L/T]

Uc			critical velocity for sediment motion in Yang (1973) relation

for total bed material load [L/T]

Uo			value of U of unperturbed base flow [L/T]

= , dimensionless flow velocity in Brownlie

(1981) relation for total bed material load [1]

critical value of  for sediment motion in Brownlie (1981)

relation for total bed material load [1]

= U/Uo, dimensionless velocity used in developing the quasi-

steady approximation [1]

u			streamwise flow velocity [L/T]

ubl			velocity of a bedload particle [L/T]

uf			flow velocity relative to particle used in computing drag force

on particle [L/T]

streamwise flow velocity averaged over turbulence [L/T]

fluctuating component of streamwise flow velocity [L/T]

, shear velocity [L/T]

, shear velocity due to form drag [L/T]

, shear velocity due to skin friction [L/T]

vs			particle terminal fall velocity in quiescent water [L/T]

vsi			fall velocity of of grain size characteristic of the ith grain size

range [L/T]

vswi			fall velocity of wash load in the ith grain size range [L/T]

fluctuating component of upward normal flow velocity [L/T]

W*			, dimensionless bedload transport rate

[1]

, dimensionless bedload transport

rate for ith grain size [1]

Xt			= (sqt/((sqt + (qw); flux-based mass concentration of

sediment (bedload + suspended load) [1]

x			boundary-attached down-channel streamwise coordinate [L]

xv			down-valley coordinate [L]

= x/Ho, dimensionless down-channel coordinate used in

studying bedforms [1]

= x/Ho, dimensionless down-channel coordinate used in

developing the quasi-steady approximation [1]

dimensionless transformed spatial coordinate used in

moving-boundary formulations of morphodynamics;

variously defined [1]

, dimensionless downstream coordinate used in

Chapter 20 [1]

y			boundary-attached transverse coordinate [L]

Zu			= , [1]

Zui			= , [1]

z			boundary-attached upward normal coordinate [L]

(x			spatial step in finite difference scheme [L]

(			coefficient corresponding to the fraction of material

transferred to the substrate as the bed aggrades that

is derived from material in the surface layer (as

opposed to bedload) [1]; also used for streamwise

angle of inclination of the bed [1].

(r			coefficient in Manning-Strickler resistance relation [1]

(t			coefficient in generic relation for total bed material load [1]

(t			time step in finite difference scheme [T]

(			tolerance for relative error used in iterative schemes [1]

(v			, thickness of viscous sublayer [L]

(			= qto/[(1 - (p)UoHo], dimensionless number used in

developing the quasi-steady approximation [1]; also

fraction relative error used in iterative schemes [1]

(s50			, used in bedload relation of Powell et al. (2001)

[1]

(sgo			=

(si			= , parameter in Parker (1990a,b) bedload

relation for mixtures [1]

(			exponent in hiding relations determining critical conditions

for the onset of motion of grains in sediment mixtures

[1]

(			channel bed elevation [L]

(base			elevation of bedrock basement [L]

(d			deviation of bed elevation from base state used in

developing the quasi-steady approximation [L]; also

downstream bed elevation at x = L [L]

= , dimensionless deviatoric bed elevation [1]

(I(x)			initial bed profile [L]

(t			elevation of the top of a bank [L]

amplitude of bed perturbation characterizing bedform [L]

= (/Ho, dimensionless bed elevation for study of bedforms

[1]

dimensionless amplitude of bed elevation perturbation [1]

= (d/Ho, dimensionless deviation of bed elevation from base

state used in developing the quasi-steady

approximation [1]

(			integral quantity relating  to qs [1]

(			transverse angle of inclination of bed [1]

(s			 = (bs/(b [1]

(			Karman constant in logarithmic velocity profile [1]

(d			kinematic diffusivity of sediment defined in Chapter 14 [L2/T]

(			wavelength of bedform [L]

(p			bed porosity [1]

(c			coefficient of Coulomb friction [1]

(			kinematic viscosity of water [L2/T]

(t			turbulent eddy viscosity for upward normal exchange of

streamwise momentum [L2/T]

(ts			turbulent eddy viscosity for upward normal exchange of

suspended sediment [L2/T]

(			water density [M/L3]

(s			sediment material density [M/L3]

upward normal Reynolds flux of streamwise momentum; = -

Reynolds stress [M/L/T2]

(			angle of inclination of bed [1]

(r			angle of repose [1]

(			arithmetic standard deviation of sediment size distribution;

same symbol also used for tectonic uplift rate [L/T]

(g			= 2(, geometric standard deviation of sediment size

distribution

(o((sgo)		functional relation in Parker (1990a,b) bedload relation for

mixtures [1]

(s			arithmetic standard deviation of surface size distribution

(b			bed shear stress [M/L/T2]

(bbf			estimate of bed shear stress at bankfull flow [M/L/T2]

(bc			critical bed shear stress [M/L/T2]

(bf			bed shear stress due to form drag [M/L/T2]

(bs			bed shear stress due to skin friction [M/L/T2]

(bscg			critical bed shear stress to move surface size Dsg [M/L/T2]

(bsci			critical bed shear stress to move size Di in surface layer

[M/L/T2]

(bsc50			critical bed shear stress to move surface size Ds50 [M/L/T2]

= (b/((RgD) or (b/((RgD50), Shields number [1]

= HbfS/(RDs50) = estimate of Shields number at bankfull flow

based on surface median size[1]

critical Shields number at the threshold of motion [1]

critical Shields number at the threshold of motion for the

limiting case of a horizontal bed (used as a basis for

determining the corresponding value for a tilted bed)

[1]

= , Shielods number based on

geometric mean bedload size [1]

Shields number of unperturbed flow [1]

, Shields number based on surface

geometric mean size [1]

, critical Shields number to move surface

size Dsg [1]

, critical Shields number to move ith grain

size in surface layer [1]

, critical Shields number to move

surface size Ds50 [1]

= reference Shields number close to (but above) the

threshold of motion [1]

, Shields number for ith grain size [1]

, Shields number for ith grain size based on skin

friction [1]

= (b/((RgDs50), Shields number used in bedload formulation

of Powell et al. (2001) [1]

critical value of  at the threshold of motion [1]

critical Shields number for the onset of sheet flow of

sediment [1]

(			uplift rate [L/T]

(			channel sinuosity [1]

(			straining parameter in Parker (1990a,b) bedload relation for

mixtures [1]

(o((sgo)		functional relation in Parker (1990a,b) bedload relation for

mixtures [1]

(			water surface elevation [L]

(bl			volume of moving bedload particles per unit bed area [L]

= (/Ho, dimensionless water surface elevation for study of

bedforms [1]

(d			downstream water surface elevation [L]

(da			ambient downstream water surface elevation before change

[L]

dimensionless amplitude of perturbation of water surface

elevation [1]

(			= , logarithmic grain size on psi scale

(b,i			=

(i			=

arithmetic grain size on the psi scale

(			= z/b; dimensionless upward normal coordinate [1]

((((((((((((((((((((((((((